## Slide 1: GDB/KGDB
Harish Chetty

## Slide 2: WHAT IS gdb/kgdb
GNU Project Debugger
Supports Windows & Linux
USES
  Pass anything to the program
  Break anywhere within the program
  Get Information about crashes
  Modify runtime values
  Reverse Engineer the Code
  Everything You Can Imagine.

## Slide 3: Setup options
Kernel Modules do not have predefined symbol locations.
GDB doesn’t understand the function and variable locations.
Only Static analysis is possible using GDB
  Must Provide the Section header address in memory.
KGDB uses 2 computers , one for testing other for debugging
  Carry out all GDB functions from debugging machine.
How to setup?
  Connect two computers using serial port
  Use virtual machine with Unix socket (and connect via serial stream).

## Slide 4: Setup Example
Not the easiest of things to set up.
This is for setting up Virtual Machine KGDB.
Target : Linux Machine (3.10.40) and Debugger : Linux Machine (3.10.40)
Debugger(Host): Virtual Machine on VMware player
Target (Client): Virtual Machine on VMware player inside Host.
Base O.S. with Windows 8.1
Different steps for different set up’s and also the virtualizing software

## Slide 5: ENABLE KGDB
It is Installed by Default
Turn it ON if not.

## Slide 6: Hardware virtualization
VT –x is Required for 64 Bit Linux.
Must be Enabled in the BIOS.
Must be Enabled in the VM.

## Slide 7: Setting up serial port in VM
ON TARGET MACHINE
Go to Settings
Create a named Socket
Use Server to An Application

## Slide 8: Unix Socket to serial listener
Since its actually a UNIX SOCKET
GDB uses serial port
socat  establish two bidirectional byte streams.
Boot the target machine, call socat from debugging machine

## Slide 9: Almost done
On Debugging machine use ‘gdb vmlinux’ .
The vmlinux is the uncompressed image of the kernel
Then set up target using:
    ‘gdb remote target /dev/pts/2’
And now we can debug!

## Slide 17: References
http://www.gnu.org/software/gdb/
https://sourceware.org/gdb/onlinedocs/gdb/Symbols.html
http://sysprogs.com/VBoxGDB/tutorial/
https://docs.python.org/2/library/pty.html
http://www.dest-unreach.org/socat/doc/socat.html
http://nam228.files.wordpress.com/2011/12/kgdb_2virtualmachines1.pdf
http://oslab.info/index.php/Misc/KGDB
http://web.cecs.pdx.edu/~jrb/cs201/lectures/handouts/gdbcomm.txt